## Slide 1: Design and Development of a Software Defined Radio Telescope
By: W. Logan Spooner and Dr. Shantanu Chakraborty

## Slide 2: Outline
Background and Premise
Circuit Setup
Horn Antenna Construction
Weather Antenna
Software
Data
Horn Antenna vs Weather Antenna
Issues and Setbacks
Looking Forward

## Slide 3: Background and Premise
21 cm wavelength radiation emitted by cold Hydrogen Clouds
  Cold Hydrogen is that which makes up most of the Inter Stellar Medium (ISM)
The observation of this helped Astronomers determine the shape and structure of our Galaxy.
We hope to create a telescope capable of observing this using a Software Defined Radio

## Slide 4: Circuit Design
SDR circuit consisted of 4 parts
  The Antenna and feedline to collect and focus the information
  A Bandpass filter (BPF) to filter out unwanted frequency bands
  A Low Noise Amplifier (LNA) to amplify our target frequency
  An RTL-SDR to allow the analysis of the data on a laptop using SDRSharp
1420 MHz BPF
LNA
RTL-SDR

## Slide 5: Horn Antenna Construction
Design comes from American Astronomical Society, AAS Meeting #224, id.415.01
Dimensions used to optimize size while still being convenient to move
Construction:
  Used a 9”x6”x4” can as the waveguide.
  5.3 cm piece of copper wire for feed line
  Cut cardboard into shape and wrapped with aluminum foil.
  Taped everything together with aluminum conducting tape.

## Slide 6: Horn Antenna Construction

## Slide 7: Weather Antenna
Noelec GOES Weather Satellite Parabolic Antenna
  1.7GHz Center Frequency
  200 MHz+ Bandwidth

## Slide 8: Software
All free open-source software used for creating software defined radios
  Limited in their use for radio astronomy
Used SDRSharp (SDR#)
  Easy UI and simple display
  Limited scope and data collection
SDRAngel was another option
  Included data save option, didn’t work properly
  More complicated UI

## Slide 9: Observation Conditions
Location: Nevins Hall roof, Valdosta State University, Valdosta, Ga.
  30.84847916421404, -83.28885987900686
Weather: Varied, mostly Sunny
Time: 10:30 EST and 22:30 EST
10:30 EST
22:30 EST

## Slide 10: Horn Antenna at Night

## Slide 11: Data: Horn Antenna in the Morning
Data from horn antenna pointed near target region.
Data as we moved away from target region.
Data when antenna was directly on our target region

## Slide 12: Data: Weather Antenna

## Slide 13: Horn Antenna vs Weather Antenna
Pros
  Directional
  Optimized for 1420 MHz band
  More customizable
Cons
  Lower gain
  Harder direction control (no mount)
Horn Antenna
Pros
  Higher gain
  Easier direction control (came with a mount)
Cons
  Wider beam angle
  Not optimized for 1420 MHz
  Less consistent data
Weather Antenna

## Slide 14: Setbacks and Limitations
Possible reflection sources
Software
  Crashes/file issues
  No obvious ways to integrate signal over time
Hardware
  RTL-SDR heating
  Angle measurement
Weather Conditions
Blue/Red shift

## Slide 15: Looking Forward
Software
  Found plugin to perform FFT (Fast Fourier Transform) of audio signal and save as Power vs Frequency
Hardware
  Parabolic dish antenna
  Larger/more precise horn antenna
  Mount with Altazimuth coordinates
Observations
  More open locations
  Other regions of the sky such as Cygnus and Sagittarius

## Slide 16: References
https://en.wikipedia.org/wiki/Hydrogen_line
http://hyperphysics.phy-astr.gsu.edu/hbase/Relativ/reldop2.html
https://www.heavens-above.com/
http://www.ccera.ca/papers/memo-0011-a-21cm-map-of-the-northern-sky/
https://radio-astronomy.org/node/191
http://mercury.pr.erau.edu/~prcphysics/observatory/hydrogen.htm